## Slide 1: An Efficient, Configurable Secure Memory Implementation
Presentation By:
Will Buziak Department of Computer Science Colorado School of Mines
February, 2026

## Slide 2: Content
Background & Motivation .............................................................3-4
Trusted Execution Environments ...................................................5-7
Secure Memory .............................................................................8-12
gem5 ............................................................................................13-25

## Slide 3: Background
Motivated attackers can employ many tactics to corrupt or steal data, this work focuses on preventing:
  A malicious OS, application or thread
  Replay or side-channel attacks targeting off-chip peripherals
Trusted Execution Environments (TEEs) provide hardware guarantees that attempt to secure the integrity of the processor
Secure Memory methods protect against off-chip tampering by encrypting and storing metadata securely on-chip

## Slide 4: Motivation
Goal: Leverage TEE architecture to implement efficient secure memory
TEEs provide confidence against malicious applications attempting to tamper with data
  Still vulnerable to replay attacks and off-chip tampering
Secure Memory can mitigate these concerns by adding another layer of protection for off-chip devices
RISC-V TEEs (e. g. Keystone[1]) provides an open-source, configurable platform for developing TEEs to specific applications

## Slide 5: Trusted Execution Environments
A TEE implements different privelege modes with separate address spaces, enforcing a set of rules dictating which components can access what regions of memory:
  User mode, Supervisor mode, Machine mode
Almost all major CPU vendors have their own flavor of TEE:
  Intel SGX/TDX
  ARM Confidential Computer Architecture
  AMD SEV
These implementations leverage proprietary hardware, opening the door for a configurable & open-source TEE, keystone[1]

## Slide 6: Trusted Execution Environments
TEEs protect the processor:
Attempts to avoid malicious activity from the application
Still vulnerable to side-channel & replay attacks
Application mode is checked on memory request:
Memory regions are assigned to modes with permissions
A region in which the mode does not have access is denied
PMP

## Slide 7: Physical Memory Protection
Each core has a PMP table:
Stores the address range along with the pmpCfg
pmpCfg determines:
Permissions, address matching, & locking with space for extra bits
PMP checks walk the table & match the request address with each stored entries A field & respective address

## Slide 8: Secure Memory
Base Assumption: off-chip data is untrusted & requires verification
Secure memory protects data / memory devices
Builds a hash ( merkle[2]) tree, the root of which is always stored on-chip
  Built over data & metadata
  Nodes can be stored in a metadata cache to reduce fetch latency
data
data
data
data
data
hmac
hmac
hmac
hmac
hmac
root

## Slide 9: Counter-Mode based Encryption
HMACs are produced through the xor of a one-time pad & the plaintext:
  One-time pad is generated with a hardware key and a write-incremented counter
  Tree must be re-hashed when counters overflow
  Counter incrementing methods reduce the frequency of rehashing the tree
AES
HW key
seed
XOR
One-time pad
plaintext
cipher text

## Slide 10: Secure Memory
Process: Off-chip data is signed with a counter, cryptographically hashed and stored in a merkle tree
  Memory blocks are fetched, hashed and compared against each successive parent node from the data leaves up to the secure root
SOC
data
data
data
data
data
hmac
hmac
hmac
hmac
hmac
Metadata-Cache

## Slide 11: Secure Memory
Process: Off-chip data is signed with a counter, cryptographically hashed and stored in a merkle tree
  Memory blocks are fetched, hashed and compared against each successive parent node from the data leaves up to the secure root
  This incurs peripheral node fetch latencies
SOC
data
data
data
data
data
hmac
hmac
hmac
hmac
hmac
Metadata-Cache

## Slide 12: Counter-Mode based Encryption
Hashing:
  Generating the one-time pad
  Refers to the mac
  mac_queue
Encryption:
  Masking the plaintext with the one-time pad
  Refers to the encryption or cipher
  cipher_queue, xor_queue
HMAC is the final cipher text
AES
HW key
seed
XOR
One-time pad
plaintext
cipher text
Counter goes here
Data (can be counter)
HMAC

## Slide 13: Secure Memory
Bonsai merkle trees[3] are built solely over the counters:
  Reduces metadata storage requirements
  Each node can protect a larger block of memory
hmac
hmac
hmac
hmac
hmac
cntr
cntr
cntr
cntr
cntr
SOC
Metadata-Cache

## Slide 14: gem5
gem5 supports RISC-V & multi-core simulation
  Keystone including PMP tables & checker implementations
  Memory encryption engine
  Secure memory implementation
Developer space is divided into different scopes
cpp Implementation
Python Wrapper
Hardware Description
Config Files
User Space
Program Binary

## Slide 15: gem5 eventQueue
The eventQueue is how gem5 schedules processes to enable multi-core simulation
  Most member functions operate shared queues instead of directly calling one another
  eventWrappers are scheduled instead
Events are scheduled with latencies:
  i.e. things like computing the cipher arent actually done, but scheduled & the latency is modeled

## Slide 16: initiateMac & initiateCipher
Prepare the pkt for hashing:
  Assigns pkt with a time signature & inserting into the hashing_queue / cipher_queue
  Schedules a mac/cipher event for the eventQueue to trigger the mac/cipher engine
initiateCipher must also account for counter vs data mac pkts:
  Control flow to insert into separate queues and handled by cipherEngine

## Slide 17: macEngine & cipherEngine
Process one pkt from respective queue & schedule the next:
  Calls handleTreeResponse / handleCounterResponse
- These in turn can call initiateCipher/Mac on the child
  Calls updateTree and responds to the processor

## Slide 18: updateTree
Creates packets for counters, mac & parent:
  Sends nodes to memory & metadata cache
  Data has been encrypted & hashes computed, all stored in the pkt
calculateAddress functions operate on the packet to return the desired address
cntr
cntr
cntr
cntr
cntr

## Slide 19: handleRequest
Prepare counter & mac for the pkt
  Place into queues for authentication
  Send to memory / metadata cache
This starts the recursive hashing / authentication
Writes are just placed in a queue

## Slide 20: handleResponse
Decryption & authentication of responses from memory requests
  Handle functions prepare pkts by checking, popping and placing into queues
  Uses other functions to actually schedule
The important / complex thing to consider in all scenarios is the coontext of control flow
  Debugging, development & code reading

## Slide 21: Port functions
Functions like sendPacket & recvRespRetry manage blocked packets in a similar manner:
  Pop / push pkts onto a blocked_packets & pending_* queues
  Calls handle functions
Important to consider the scope of the call (mem_side vs cpu_side)

## Slide 22: handleCounterResponse
Check for data waiting on the counter:
  Send for encryption / decryption
  If pkt is a write, compute the MAC

## Slide 23: handleMacResponse
Check for returned data waiting on a counter
  Push onto pending_mac queue

## Slide 24: handleTreeResponse
Handles the recursive authentication of the integrity tree
  Parent and all children nodes are authenticated
  Authenticates metadata & sends to metadata cache
  Mostly removes eligible pkts from needs_authentication queue

## Slide 25: handleMetadataCacheMiss
Adds pkt to authentication queue
  Checks for eager fetch and sends parent pkt to metadata cache
  Must be metadata

## Slide 26: Conclusion
Everything is stored and processed through the pkt
The eventQueue schedules processes
  Functions operate on shared queues in order to service pending pkts
The state of the system is the important thing to debug as problems arise and implementations progress

## Slide 27: Sources
[1] Dayeol Lee (2022) Building Trusted Execution Environments. In: A dissertation submitted in partial satisfaction of the requirements for the degree of Doctor of Philosophy in Computer Science in the Graduate Division of the University of California, Berkeley.
[2] Chenyu Yan, Brian Rogers, Daniel Englender, et. al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. In: Proceedings of the 33rd International Symposium on Computer Architecture (ISCA’06)
[3] Brian Rogers & Milos Prvulovic (2007) Using address independent seed encryption and bonsai merkle trees to make secure processors OS-and performance-friendly. In: 40th IEEE/ACM International Symposium on Microarchitecture (MICRO’07)
[4] Zach Moolman & Tamara Silbergleit Lehman (2024) Extending RISC-V Keystone to Include Efficient Secure Memory
[5] The RISC-V Instruction Set Manual: Volume II Privileged Architecture. Version 20240411
[6] Samuel Thomas (2025) Towards A Practical Secure Memory for Practical Development

## Slide 28: Where does Secure Memory fit in?
Secure Memory
RISC-V Keystone
Application Thread
Operating System
Remote or Cloud User
Potentially Malicious
Storage
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
Secure memory methods protect SoCs against off-chip memory corruption by additionally:
  Encrypting / Decrypting protected memory
  Storing and checking an integrity tree to verify data
These checks result in latencies both in encryption and memory

## Slide 29: Secure Memory Incurs Latency
Secure Memory
RISC-V Keystone
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
An integrity tree, or Merkle tree, is simply a hash tree
  Each parent is the hash of its children
  Root is kept on-chip
On a memory fetch, the core must additionally:
  Check that the data hash matches a leaf and the parent has not been tampered with
  Recursively check each node up to the root
data
data
data
data
data
hash
hash
hash
hash
hash

## Slide 30: Secure Memory Incurs Latency
Secure Memory
RISC-V Keystone
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
An integrity tree, or Merkle tree, is simply a hash tree
  Each parent is the hash of its children
  Root is kept on-chip
On a memory fetch, the core must additionally:
  Check that the data hash matches a leaf and the parent has not been tampered with
  Recursively check each node up to the root
data
data
data
data
data
hash
hash
hash
hash
hash

## Slide 31: Secure Memory Incurs Latency
Secure Memory
RISC-V Keystone
Chenyu Yan, Brian Rogers, Daniel Englender, et al. (2006) Improving Cost, Performance, and Security of Memory Encryption and Authentication. (ISCA’06)
An integrity tree, or Merkle tree, is simply a hash tree
  Each parent is the hash of its children
  Root is kept on-chip
On a memory fetch, the core must additionally:
  Check that the data hash matches a leaf and the parent has not been tampered with
  Recursively check each node up to the root
data
data
data
data
data
hash
hash
hash
hash
hash

## Slide 32: Keystone Memory Isolation
On boot, the Security Monitor (SM) sets up a component called the Physical Memory Protections (PMP) Table:
Divides memory and assigns to modes
Resides in each core
If a memory request from an application does not have access, it is denied
RISC-V Keystone
Application Thread
Operating System
Remote or Cloud User
Potentially Malicious
Dayeol Lee, David Kohlbrenner, Shweta Shinde, Krste Asanovic, and Dawn Song, Keystone: An Open Framework for Architecting Trusted Execution Environments, EuroSys 2020.
PMP
DRAM

## Slide 33: Extending Keystone to include Efficient Secure Memory
To mitigate latency concerns, our work proposes to store metadata on-chip, greatly reducing memory access overhead
This structure is called the Aggregated Extended PMP (ePMP) table:
Tracks requests through the Memory Encryption Engine (MEE)
Updates metadata entries corresponding to their PMP status
DRAM
Zach Moolman & Tamara Silbergleit Lehman, Extending RISC-V Keystone to Include Efficient Secure Memory CARRV 2024
Memory Encryption Engine
ePMP
RISC-V Keystone

## Slide 34: Extending Keystone to include Efficient Secure Memory
To mitigate latency concerns, our work proposes to store metadata on-chip, greatly reducing memory access overhead
This structure is called the Aggregated Extended PMP (ePMP) table:
Tracks requests through the Memory Encryption Engine (MEE)
Updates metadata entries corresponding to their PMP status
DRAM
Zach Moolman & Tamara Silbergleit Lehman, Extending RISC-V Keystone to Include Efficient Secure Memory CARRV 2024
Memory Encryption Engine
ePMP
RISC-V Keystone
CPU
SoC

## Slide 35: The gem5 Simulation Suite
gem5 is an open-source, cycle-accurate architecture emulation platform
Allows end-to-end development including full-system simulation & benchmarks
Breaks hardware description into different layers, enabling researchers to edit any aspect of an implementation
This is helpful, but also results in a colossal codebase
Jason Lowe-Power, Abdul Mutaal Ahmad, Ayaz Akram, Mohammad Alian, et al. (2007), The gem5 Simulator: Version 20.0+ (arXiv)
cpp Implementation
Python Wrapper
Hardware Description
Config Files
User Space
Program Binary

## Slide 36: Challenges with gem5
Linux Kernel
Disk Image
gem5 Pre-compiled Resources
Boot-loader
This work requires the use of gem5 full-system emulation, while many aspects of gem5 enable research, some also hinder progress
  Scattered source files
  Lots of detail, making high-level understanding non-trivial
  FS requires gem5 resources and pre-compiled binaries

## Slide 37: Direction / Future Work
Implementing a RISC-V TEE in gem5:
  Currently adding cache hierarchy
    Incorporating caches into secure memory through “board” hierarchy
    Entirely different way of connecting things
  PMP is included in any RISCV cpu in gem5
What is my contribution?
  Until now, I have been just trying to implement Zach’s work in gem5
  Deeper understanding of attack methods (winter break project?)
Moolman, Z. & Lehman T.

## Slide 38: Gap & Contribution
A Midsummer Nights Tree (AMNT) by Sam Thomas
  Crash consistent secure memory protocol by defining write-back protocols that sync the on-chip BMT root & stored leaf counters in off-chip memory

## Slide 39: Limitations
Computational and memory overhead

## Slide 40: PMP Sensitivity Analysis
How does a variable PMP size affect performance
Efficient PMP packing:
  Currently, gem5 implements Naturally Aligned Power of Two (NAPOT) packing, which requires the base address to be aligned by a power of two.

## Slide 41: gem5 Simple Sanity Check
Base gem5 vs. Secure Memory implementation (version 24.0.0.1)
Benchmark:
  1,000 accesses on 1GB array of memory
  No caches
Secure memory implementation requires an increase in both runtime and memory overhead
 | Simulated Time (Seconds) | Host Memory (MB) | Number of Instructions (thousands)
Base gem5 | .00388 | 1.18 | 55,966
Secure gem5 | .014 | 3.43 | 55,966

## Slide 42: gem5 Cache Sanity Check
Base gem5
Secure gem5
False
True
False
True
Simulated Time (seconds)
Host Memory (MB)
Number of Instructions
.003880
1.18
55,966
.000069
1.18
55,966
.014
3.43
55,966
.000531
3.44
55,966
Cache